## Slide 1: Implementation of Hardware monitoring using Ethernet LwIP.
By
Rithvik Ballal
Tejas Chavan

## Slide 2: IN A NUTSHELL Remotely monitoring a hardware through the network. We will be using an Ethernet LwIP core to establish a point to point connection between the client and server. Build an Ethernet based Hardware to create a server using the microblaze softcore. Develop a QT based GUI application to create a client system that would ask for connection with the server in order to access a resource (Hardware) This client server relationship is established using the LwIP stack which is a lighter implementation of the TCP/IP stack. Once the connection is established packets can be transferred between the server and the client to monitor the hardware.

## Slide 3
HARDWARE AND SOFTWARE USED:
Pmod-HB3 Motor driver – The motor is a computer fan running at 12V DC
Pmod-HYGRO – Temperature and Humidity sensor.
        The temperature and humidity of the environment is sensed and sent to client
        Ethernet cable
        QT application GUI – The QT based application is used to create a GUI to act as a client.

## Slide 4
Block Diagram

## Slide 5
SOCKET PROGRAMMING
Socket: Create a new connection endpoint
Bind : Attach a local address to a socket
Listen : Announce willingness to accept a connection
Accept : Block caller until a connection request arrives.
Connect: Actively attempt to establish a connection.
Send: Send some data over the connection.
Receive : Receive some data.
Close: Release the connection.

## Slide 6
SERVER
CL
I
ENT
0x02 <data>
0x03 0x00
0x04 <data>
0x00
0x05
give_Temp_deg(16 bits)
Ask_Temp_deg(16 bits)
Ask_Temp_humid(16 bits)
give_Temp_humid(16 bits
0x00 <data>
send_duty_cycle(16 bits)
GENERALIZED PACKET FORMAT

## Slide 7
Getting started with the QT application builder.
Getting familiar with socket programming.
Data conversion between UNICODE to ASCII.
Synchronization when continuous packets are being transferred or received.
CHALLENGES FACED:

## Slide 8
WORK DISTRIBUTION:
Rithvik : Building the Client side of the system.
Developing QT application GUI to interact with the server.
Tejas : Building the hardware using microblaze to get the ethernet up.
Performing Socket Programming to establish connections between the server and client.

## Slide 9: APPLICATIONS: Monitoring Machineries in industries from a remote location. Home Automation. *******************************************************